## Slide 1
EV FireSafe
Enhancing safety for emergency responders at electric vehicle fires
EV FireSafe
Supported by:
With assistance from:
evfiresafe.com
EV Extrication
High level considerations
Developed in collaboration with the Victorian State Emergency Service

## Slide 2
As electric vehicles become commonplace, the emergency response community worldwide will see collisions & thermal events (battery fires) more frequently.
From a patient extrication perspective, what do we know & what do we need to learn about rescuing someone from an electric vehicle, compared with a traditional internal combustion engine vehicle?
EV extrication

## Slide 3
What's an electric vehicle?
Nissan Leaf BEV
Hyundai Ioniq
(BEV & PHEV)
Mitsubishi Outlander PHEV
Hyundai Kona (BEV & PHEV)
Tesla Model 3 BEV
Battery electric vehicle
100% electric
BEV
MG ZS EV (BEV & PHEV)
Hyundai Ioniq 5 BEV
Polestar 2 BEV
All have a high voltage traction battery (over 60V) that charges up using a cable plugged into power supply.
Plug in hybrid electric vehicle
Electric & petrol driveline
PHEV

## Slide 4
An EV battery pack is constructed with individual lithium ion battery cells:
EV battery pack construction
Lithium ion battery cell
Multiple cells make a battery module
Multiple modules make a battery pack, which is enclosed in protective battery casings

## Slide 5
Battery pack location
In passenger EVs, the traction battery supplies power for vehicle momentum & is located beneath the vehicle, between chassis rails
EV traction battery pack
HV components, such as the motor & DC:DC converter, are located around the vehicle
Orange cables connect HV components & battery together

## Slide 6
What is stranded energy?
Even after responders isolate high voltage (HV) systems, the risk of fire & electrocution from stranded energy remains
Stranded energy still exists in the HV battery, isolation just stops it moving around the HV systems (battery to components, via cables)
Even at 0% state of charge, an EV battery cell holds 2.4V. Stranded energy describes power within a battery cell that cannot be de-energised.

## Slide 7
  HV battery
  Electric motor
  Inverter
  BMS / VCU
  Charge port
  DC:DC converter
  Cables
High voltage - marked in orange (>60V)
  Doors
  Windows
  Lights
Low voltage - 12V
Electrocution - low risk
Charging unit
  AC grid power - same as a mains connection
Responders cannot detect HV & there is no way to de-energise

## Slide 8
Thermal runaway
If battery cells are abused they may go into thermal runaway, leading to fire &, in very rare cases, a vapour cloud explosion.
The cell short circuits & heats up
Pressure (in the form of gases) escapes via cell safety valve
Ignition or vapour cloud explosion occurs
A battery cell suffers abuse
(ie. traffic collision)
Other nearby cells heat up
Other cells follow
Approx 170 c
o
Approx 50-60 c
o
Highly toxic & flammable gases
(30-50% hydrogens)
Thermal runaway can occur very quickly.

## Slide 9
Thermal runaway - fire / explosion
Rescuers should be constantly assessing for the signs of thermal runaway & should evacuate immediately if they see or hear any of these signs.
Ignition
Jet like, directional flames
Vapour cloud explosion
Violent deflagration
~90%
~10%
At this point, one of two things will occur
Popping - gunshots
Hiss/whistle - gas venting
'Cherry bubblegum' smell
Projectiles - cell debris
Dark vapour cloud,
light vapour cloud
(it's NOT smoke)
Both pose a serious risk to rescuer safety

## Slide 10
Vapour showing
Vapour cloud explosion
Elapsed time: 10 seconds
Case study
Tesla Model S parked in underground residential apartment building carpark. Battery had been damaged 30 minutes earlier after driving into an open manhole cover.

## Slide 11
Thermal runaway - DRA
Incident controllers managing EVs should consider a dynamic risk assessment throughout the entire incident duration:
  Requesting firefighters even for minor incidents
  Lay & charge hose lines for immediate battery cooling &/or suppression
  Ensure BA Operators are standing by
  Monitoring with TIC of HV battery pack (underside of EV) for increasing heat
  Constantly monitoring for signs of thermal runaway until vehicle handover
We've used this image throughout this pack to remind responders of the need to CONSTANTLY monitor for signs of thermal runaway

## Slide 12
EV identification
Assume you're dealing with an electric vehicle until proven otherwise:
  Look for:
    Blue EV badge on numberplates
    External badging saying 'electric', 'low emissions', 'PHEV', 'EV'
    Ask driver &/or passengers
  Use ‘EV’ tape to immediately identify to all responders attending
  Find relevant ERG, via CRS, ANCAP Safety App or online
TR DRA
No grille
Badging
Charge port
No exhaust
Badging
Numberplate badge

## Slide 13
Approach
TR DRA
As responders approach an electric vehicle, remember:
  There may be no engine noise
  EV may move silently & rapidly
  Consider approaching from a 30% angle (similiar to a BLEVE approach) to avoid responder injury from suddenly moving vehicle

## Slide 14
Exposures
Rescuers should look for:
  ORANGE HV cables – EVs run at 400V & above
  Battery cells exposed or scattered – these present an electrocution risk
  Dark patches on battery pack (underside) that may indicate rapid heat build up
  Obvious damage to the battery pack
  Fluids on ground
TR DRA

## Slide 15
Immobilise
Electric vehicles can move silently & with instant speed. Rescuers should:
  Ensure you have correct ERG for the EV make & model
  Chock wheels - truck-sized chocks may be needed to adequately hold EV in place
  If possible:
    Engage with driver
    Put EV into park
    Push On/Off button
    Remove proximity keys
Note: Tesla EVs primarily use drivers smartphone as a key, but may also use a 'card' key' or a finger ring. They do not have an On/Off button.
TR DRA

## Slide 16
Isolate high voltage systems
To make the EV safer to work around, rescuers should isolate low voltage (LV) & high voltage (HV) systems.
  LV 12V battery:
    Ensure doors / windows / bonnet / boot are open if required – these cannot opened once 12V disconnected
    Review ERG to locate & disconnect 12V battery to disable SRS
  HV traction battery:
    Review ERG for isolation method for HV system specific to EV
      Responder cut loop - use 18 inch insulated bolt cutters
      Responder pull fuse - refer to your agency for PPC requirements
LV: 12V battery typically located under bonnet or underfloor of boot
HV: >60V traction battery that gives EV momentum
TR DRA

## Slide 17
HV systems should automatically isolate upon impact involving safety systems (airbags, seatbelt pretensioners)
Isolate high voltage (HV) systems
Where available, also conduct manual isolation of HV systems for additional safety while extrication is taking place
When LV (12V) system is disconnected, contactors to the HV system should remain in the ‘open’ position, thereby isolating HV
Note:
Risk of electrocution remains!

## Slide 18
Rescue responder protection
TR DRA
To enhance rescue responder protection:
  Monitor HV battery pack (underside of EV) with TIC to detect rising heat
  Lay & charge hose lines for battery cooling &/or suppression
  Ensure BA Operators are standing by

## Slide 19
Stabilisation
TR DRA
An EV HV battery is heavy & EVs may be more likely to stay on wheels:
  EV average kerb weight 1800kgs
  HV battery average weight 550kgs
EV on wheels:
  Consider where block & wedge stabilisation will go
  Add EV tape to battery pack for visible reminder (if possible)
EV on side:
  Use side stabilisation with multiple wedges
  Underside stabilise forward of front tyres & rear of rear tyres
  Consider construction – soft materials like aluminium & kevlar may rip if used as an anchor (eg. Tesla bonnet is light aluminium)
  Add EV tape to battery pack for visible reminder
EV on roof:
  Similar to all ICE vehicles
  Consider access to HV cut loop or pull fuse for HV disconnection
  Add EV tape to battery pack for visible reminder (if possible)

## Slide 20
Stabilisation (con't)
  Relocation considerations (if on wheels)
    Roll EV away from structures to enable access to patient
  Check ERGs & look for hoisting points on EVs which provides 4 point stabilisation
  5th point stabilisation – depends incident type
Note: Do not touch, push off or penetrate the HV battery pack area (shown in grey), which sits along the floor pan between chassis rails on all passenger EVs. Stick outside of battery zone – front & rear of tyres

## Slide 21
Glass management
Glass may form part of the structural integrity of EV
  Tempered breaks into small pieces / laminated breaks as slab glass
  Check ERG for glass type (side laminated glass) that may need to be removed/managed to reach HV disconnects etc
    Use beluga tool for laminated glass
    Use windscreen splinter guard
  Cutting laminated glass leads to glass dust and needs to be managed accordingly
  Casualty protection (soft/hard) & sharps protection
TR DRA

## Slide 22
Gaining access & extrication
Rescuers should consider:
  Further review of the ERG for vehicle schematics
  That traditional entry &/or cutting points may vary in an EV
  Expose / Investigate before commencing tool operations
  Ramming off vehicle floor may cause battery abuse leading to thermal runaway.
    Consider placement of ram supports
    If using cross rams, consider penetration of ram into car & HV cable locations
  Refer to ERG for location of AC/DC converter, which may be located in EV footwell
  EV airbags, seats & vehicle controls are managed similarly to other vehicles
  Existing techniques
    Check the basics
      Open doors or ask occupant to open locked doors
      Use manual override latch (Check ERG)
TR DRA
Passenger EV HV battery is located between chassis rails, along floor pan

## Slide 23
Gaining access & extrication (con't)
Extrication via doors using rattle / spread / cut method:
  From front:
    manipulate front guard to expose hinges & check for HV cables
  From rear:
    consider working tool along door edge to access Nader bolt to minimise skinning doors, checking vehicle construction & for HV cables
  Consider potential for gull wing doors – only in Tesla Model X
  Consider power assisted doors, such as tailgate

## Slide 24
Gaining access & extrication (con't)
Side extrication:
  Remove both doors then B pillar, referring to ERG for location of HV cables
Rear extrication
  If possible, wind windows down to minimise cutting side laminated glass windows.
  DRA Glass roof - Remove / leave?
Ramming:
  B to A - Dash roll
    Consider relief cut location with vehicle HV systems?
  Internal - Floor, Dash / Doors
    Refer to ERG for locations of HV systems.
Dash Lift:
  Refer to ERG & consider:
    EV cables
    Vehicle construction
    Pushing off HV systems (expose first) & pushing off floor pan (risk of damaging battery cells)
Model 3 / Y rocker / door sill

## Slide 25
Patient packaged
TR DRA
Once extrication is complete, package patient for delivery to medical team

## Slide 26
TR DRA
Conclude rescue & handover
Consider potential contamination of PPC / PPE & follow agency clean up procedures
  Incident controller should make towing / recovery aware vehicle is electric
    Provide make, model & ERG for towing instructions if required
  Use ‘EV’ tape for immediate identification
  Brief investigators on modifications made, such as cut seat belts, HV isolation cut loop etc
Example only, refer to your agency for guidance

## Slide 27
Body recovery
TR DRA
Rescuers should keep all previous considerations in mind:
  Fire agencies should remain on scene to provide charged line for immediate suppression & cooling
  BA operators should be on standby
  Responders should brief controlling agency for investigation on inherent EV risks
  Fire to remain on scene until EV has been handed over to towing/recovery

## Slide 28
Post incident
TR DRA
  EV tape for immediate identification
  Ensure towing / vehicle recovery personnel are aware vehicle is electric
    Storage / tow yards should consider keeping damaged EVs separated from other vehicles due to risk of secondary ignition

## Slide 29
Emma Sutcliffe
Project Director
emma@evfiresafe.com
0409 040 499
evfiresafe.com
Scan with your smart phone camera to jump to the EVFS website